## Slide 1
WOBBLE
MECHANISMS
A mechatronic egg that turns imbalance into choreography
ESP32 · BNO055 · TMC2209 · stepper actuation · laptop dashboard
A technical prototype for sensing, self-righting motion,
and delayed response between two expressive objects.
WOBBLE MECHANISMS / FINAL PRESENTATION SOURCE

## Slide 2
02
How to read this project
Five chapters: from desire to evidence
WOBBLE MECHANISMS / TECHNICAL PROTOTYPE
01
ART MOTIVATIONS
Why an egg should feel alive
02
TECHNICAL VISION
What must be sensed, modeled, and controlled
03
REALIZATION + DEMO
Firmware, dashboard, hardware, and measured behavior
04
FUTURE DIRECTIONS
What must be instrumented next
05
LEARNING
The assumptions that changed

## Slide 3
01
ART MOTIVATIONS
A small body becomes expressive when its constraints become gestures.
WOBBLE MECHANISMS / CHAPTER

## Slide 4
04
Product concept
A self-righting object with a visible inner life
WOBBLE MECHANISMS / TECHNICAL PROTOTYPE
IDLE
→
INITIATE
→
WOBBLE
→
SETTLE
• Independent distance, smooth-distance, and rocking modes
• IMU tare, stop, immediate stop, and clockwise origin return
• Second egg can answer with a delayed, lower-intensity motion
• Implemented behavior is verified; final product experience remains a design direction
TWO EGGS = A CONVERSATION
one initiates
one listens
one answers
both settle

## Slide 5
05
Why an egg?
Passive self-righting becomes an active control problem
WOBBLE MECHANISMS / TECHNICAL PROTOTYPE
τgravity = m g dCoM sin(θ)
• Bottom-heavy geometry creates a restoring torque
• The motor injects motion around the stable equilibrium
• Tilt angle depends on mass distribution, contact, friction, and excitation
• A static lean is not the same as a dynamic wobble
gravity ↓
CoM
contact point
θ

## Slide 6
02
TECHNICAL VISION
Make a physical intuition inspectable: geometry → sensing → control → evidence.
WOBBLE MECHANISMS / CHAPTER

## Slide 7
07
Iterations and design-space exploration
From mechanism research to a working two-board prototype
WOBBLE MECHANISMS / TECHNICAL PROTOTYPE
• Explore ten actuation architectures
• Model egg dynamics and motor methods
• Add ESP32 + BNO055 + TMC2209 control
• Build USB dashboard and independent board routing
• Add peer filtering and delayed follower behavior
• Prototype Wi-Fi, then return to USB for deterministic commissioning
• Add live plots, session capture, and smooth motion
10 explored architectures
eccentric mass
solenoid slider
EAP / hydraulic piston
voice coil / reactive pendulum
piezo / SMA
BLDC cam
adaptive resonance

## Slide 8
08
Current prototype architecture
Sensing, actuation, and laptop control
WOBBLE MECHANISMS / TECHNICAL PROTOTYPE
VISUAL ASSET
system-architecture.svg
BNO055 → ESP32 MicroPython → TMC2209 STEP/DIR/EN → stepper → mechanism
• Egg A and Egg B have independent command paths
• Telemetry returns IMU and motor state
• Peer mode is relayed through the laptop
• USB is the primary working transport

## Slide 9
09
Final technical stack
The prototype spans embedded, host, and communication layers
WOBBLE MECHANISMS / TECHNICAL PROTOTYPE
EMBEDDED
• ESP32 MicroPython
• BNO055-compatible IMU
• TMC2209 STEP/DIR
• Two-phase stepper
HOST
• Python + pyserial
• HTML / JavaScript dashboard
• NumPy / SciPy
• PyBullet / Matplotlib
COMMS
• USB serial JSON
• Wi-Fi HTTP experiment
• ESP-NOW logic prototype
• Laptop-relayed peer mode

## Slide 10
10
Dashboard concepts
The UI is a measurement instrument, not just a remote control
WOBBLE MECHANISMS / TECHNICAL PROTOTYPE
IMU
Inertial Measurement Unit
BNO055 estimates orientation, acceleration, and angular velocity.
GYRO
Angular velocity
How fast the body is rotating; reported in degrees per second.
ACCEL
Specific force
Includes gravity; dynamic acceleration estimates motion beyond ~1 g.
RPM
Shaft speed
Motor tempo; at 3200 steps/rev, RPM × 3200 / 60 = step rate.
TARE
Reference pose
Stores the current IMU reading as zero for relative orientation.
ORIGIN
Motor pose
Stores a shaft step reference; separate from IMU tare.

## Slide 11
11
Repository structure
Where the system lives
WOBBLE MECHANISMS / TECHNICAL PROTOTYPE
wobble_mechanisms/
├── simulator/src/ physics and egg model
├── simulator/firmware/ ESP32 firmware + BNO055
├── simulator/dashboard/ USB bridge, UI, plots
├── simulator/wifi_dashboard/ separate HTTP experiment
├── simulator/dual_board/ peer / ripple logic
├── simulator/wired_tests/ physical logs
├── simulator/docs/ deck, diagrams, assets
└── simulator/datasheet/ motor references
Color key
model
firmware
physical tests
coordination

## Slide 12
12
PCB / electronics integration
A documented schematic, not yet a manufactured PCB
WOBBLE MECHANISMS / TECHNICAL PROTOTYPE
VISUAL ASSET
egg-unit-sheet1-schematic.svg
• ESP32 controller
• BNO055 I²C: SDA 21, SCL 22
• TMC2209: STEP 25, DIR 26, ENN 27
• Separate VMOT and regulated ESP32 logic supply
• Common ground
STATUS: schematic / wiring asset
No verified layout, Gerbers, or manufactured PCB in repo.

## Slide 13
13
Motion primitives and units
The firmware controls travel and timing; the IMU observes body motion
WOBBLE MECHANISMS / TECHNICAL PROTOTYPE
RUN
one-way motion
to target distance
SMOOTH
pre-target braking
before endpoint
ROCK
alternating direction
finite or continuous
200 full steps/rev × 16 microsteps = 3200 commanded steps/rev
0.05 rev = 160 commanded steps · 1.00 rev = 3200 commanded steps
Software steps are not proof of physical shaft motion without an encoder or marker.

## Slide 14
03
REALIZATION + DEMO
A command becomes pulses, pulses become motion, and motion becomes evidence.
WOBBLE MECHANISMS / CHAPTER

## Slide 15
15
Gyro, acceleration, speed, and rocking
Four signals that describe different parts of a motion event
WOBBLE MECHANISMS / TECHNICAL PROTOTYPE
GYROSCOPE
angular velocity · °/s
Primary peer-motion signal
ACCELEROMETER
specific force · includes gravity
Dynamic motion beyond 1 g
RPM
motor shaft speed
Tempo and inertial excitation
ACCELERATION
RPM change rate · RPM/s
Gesture sharpness / vibration
dynamic_accel = abs(|accel| − 9.80665 m/s²)

## Slide 16
16
Smooth-motion visualization
Normal motion versus controlled pre-target braking
WOBBLE MECHANISMS / TECHNICAL PROTOTYPE
NORMAL
ramp → cruise → abrupt stop
Higher endpoint impulse
More excitation at reversal / stop
SMOOTH DISTANCE
ramp → cruise → brake → settle
Uses remaining distance and acceleration
to reduce endpoint impulse
Capture and plot with dashboard/capture_session.py and dashboard/plot_session.py

## Slide 17
17
Firmware realization
The control loop is deliberately legible
WOBBLE MECHANISMS / TECHNICAL PROTOTYPE
Command parser → Stepper state machine → PWM frequency → telemetry
if mode == "smooth_run":
remaining = target_steps - abs(position_float_steps)
braking_rpm = sqrt(remaining * 120 * accel / steps_per_rev)
desired_rpm = min(cruise_rpm, braking_rpm)
ramp(rpm, desired_rpm, accel, dt)
pwm.freq(round(rpm * steps_per_rev / 60))
{"cmd":"smooth_run","rpm":10,"accel":10,
"distance_rev":0.05,"direction":1}
→ 160 commanded steps
→ telemetry at ~30 Hz

## Slide 18
18
Peer realization
A ripple is a signal-processing pipeline, not a direct mirror
WOBBLE MECHANISMS / TECHNICAL PROTOTYPE
gyro_score = clamp(norm(gyro) / 90, 0, 1)
accel_score = clamp(dynamic_accel / 2.5, 0, 1)
raw = 0.70 * gyro_score + 0.30 * accel_score
filtered = EMA(raw, tau=0.18)
rock = hysteresis(filtered, start=.18, stop=.10)
• 250 ms intentional delay
• Follower intensity defaults to 50%
• Stale packets stop the follower
• Duplicate rock starts are suppressed

## Slide 19
19
Coordination algorithm
A filtered, delayed, reduced-intensity response
WOBBLE MECHANISMS / TECHNICAL PROTOTYPE
IMU sample
gyro + dynamic accel
weighted score
EMA τ = 0.18 s
hysteresis
250 ms delay
50% follower
rock intent
gyro_score = clamp(|gyro| / 90 dps, 0, 1)
accel_score = clamp(dynamic_accel / 2.5, 0, 1)
raw_score = 0.70 gyro_score + 0.30 accel_score
Safety behavior
sequence validation · stale timeout · duplicate suppression · local stop

## Slide 20
20
Live plots and physical validation
Concrete unloaded-board evidence, with explicit limits
WOBBLE MECHANISMS / TECHNICAL PROTOTYPE
VISUAL ASSET
physical-validation.svg
• 0.05 rev finite motion reached 160 steps
• Continuous rocking stop latency: ~110–113 ms
• Full-circle software runs reached ±3200 steps
• IMU telemetry ran concurrently with PWM stepping
• Observed unloaded-board temperature: ~31–32 °C
These results validate the command path and telemetry.
They do not certify loaded mechanics or missed-step rate.

## Slide 21
04
FUTURE DIRECTIONS
The next prototype should reduce uncertainty, not simply increase speed.
WOBBLE MECHANISMS / CHAPTER

## Slide 22
22
Failed attempts and engineering lessons
Separating transport, power, software, and physical assumptions
WOBBLE MECHANISMS / TECHNICAL PROTOTYPE
WI-FI
heartbeat watchdog + hotspot compatibility
POWER
TMC VDD does not power the ESP32
MOTION
software steps can advance without shaft motion
IMU
wiring, 3.3 V integrity, EMI, or address mismatch
USB became the deterministic commissioning path; Wi-Fi remains a separate experiment.

## Slide 23
23
Validation boundary
Simulation → unloaded board → loaded mechanism → product
WOBBLE MECHANISMS / TECHNICAL PROTOTYPE
01
SIMULATION
model approximations
→
02
UNLOADED BOARD
command + telemetry
→
03
LOADED MECHANISM
tilt, thermal, missed steps
→
04
PRODUCT
repeatability + packaging
Do not present simulated rankings or software position as final physical performance.

## Slide 24
24
Artistic vision
Personality, sustained presence, and movement as conversation
WOBBLE MECHANISMS / TECHNICAL PROTOTYPE
The egg should feel like a small character.
Not a face. Not a voice. A recognizable way of moving.
• PERSONALITY — cautious, curious, confident, tired
• SUSTAINED MOVEMENT — a state, not a one-shot trick
• INTERCONNECTION — listen, delay, answer, drift
MOTION AS RELATIONSHIP
Egg A moves
↓ listen
Egg B answers later
↓ soften
Both settle / continue
Perfect synchronization = duplication
Delay + variation = personality
ACCELERATION
gesture sharpness
RPM
tempo
AMPLITUDE
intensity
DELAY
anticipation

## Slide 25
25
Future engineering steps
The next milestone is proving loaded mechanical behavior
WOBBLE MECHANISMS / TECHNICAL PROTOTYPE
• Add a shaft marker or encoder; measure missed steps
• Measure shell mass, center of mass, inertia, and linkage ratio
• Validate ESP32 power and TMC current limits
• Measure loaded tilt, natural frequency, temperature, repeatability
• Create production PCB design with protection and test points
• Mature peer transport after independent motion is reliable
PROTOTYPE
→
INSTRUMENTED
PROTOTYPE
→
DEPLOYABLE
OBJECT

## Slide 26
05
LEARNING
The useful result is not a perfect wobble; it is a better question.
WOBBLE MECHANISMS / CHAPTER

## Slide 27
27
What We Learned
Live reflection slide
WOBBLE MECHANISMS / TECHNICAL PROTOTYPE
What surprised us?
Which assumption failed?
What should the next prototype teach us?
Intentionally left open for presentation notes and audience reflection.

## Slide 28
28
Appendix / references
Evidence and implementation files
WOBBLE MECHANISMS / TECHNICAL PROTOTYPE
simulator/docs/PRESENTATION_OUTLINE.md
simulator/docs/TECHNICAL_PRESENTATION.md
simulator/docs/assets/system-architecture.svg
simulator/docs/assets/egg-unit-sheet1-schematic.svg
simulator/docs/assets/physical-validation.svg
simulator/wired_tests/physical_test_log.md
simulator/dashboard/capture_session.py
simulator/dashboard/plot_session.py
simulator/dual_board/test_ripple_logic.py