## Slide 1
WOBBLE
MECHANISMS
From restoring torque to a measured motion loop
ESP32 / BNO055 / TMC2209 / stepper actuation / USB dashboard
A bottom-heavy body turns an internal torque command into visible motion.
The dashboard closes the loop with orientation, inertial, and motor state.

## Slide 2
02
The motion loop
The technical question is how input becomes measurable wobble
Command becomes useful when the physical response is observable.
FORWARD PATH
COMMAND
JSON over USB
115200 bit/s
CURRENT
TMC2209 coil drive
I [A]
TORQUE
Stepper shaft
τ [N·m]
REACTION
Offset mass
τreaction [N·m]
WOBBLE
Egg tilt
θ [deg]
FEEDBACK / SAFETY
BNO055: orientation θ [deg] | gyro ω [deg/s] | acceleration a [m/s²] | temperature T [°C]
Dashboard observes orientation, inertial, and motor state. Stable-rock safety + peer filtering use it; ordinary run/rock remains open-loop.

## Slide 3
03
Electronics integration
The schematic is a wiring reference; the firmware test map is the current authority
SIGNALS
• I²C: SDA GPIO 21, SCL GPIO 22
• I²C clock: 100 [kHz]
• Firmware test map: STEP GPIO 25, DIR GPIO 26
• ENN GPIO 27, active low
POWER
• 12 [V] motor reference; verify installed supply; asset labels 10 [V]
• Logic 3.3 [V] + common ground
• Bulk cap 100 [µF] / ≥25 [V]; EN pull-up 10 [kΩ]
• SM-17HS4023 motor reference: 0.7 [A/phase]
• TMC2209 current limit: not recorded; verify setting
AS-BUILT NOTE
Schematic pin map unreconciled; test map: STEP 25 / ENN 27.

## Slide 4
04
Components inside one egg
Each part owns one stage of the sensing-to-motion chain
01
BNO055
IMU
orientation [deg], acceleration [m/s²], gyro [deg/s]
02
ESP32
controller
parses JSON, schedules motion, emits telemetry
03
TMC2209
driver
regulates phase current [A] at a hardware-configured limit; STEP / DIR / ENN provide pulse, direction, enable
04
STEPPER
actuator
SM-17HS4023 ref: 0.7 [A/phase] → shaft torque [N·m]
05
MECHANISM
body + offset mass
converts internal reaction torque into tilt [deg]
BNO055 → ESP32 → TMC2209 → stepper → mechanism → BNO055

## Slide 5
05
Mechanical design: load path + center of mass
Mass properties, bearing support, and contact geometry determine how torque becomes visible wobble
MECHANICAL LOAD PATH
MOTOR / SHAFT
τmotor [N·m]
BEARING SUPPORT
radial + axial load [N]
OFFSET MASS
r [m]
internal mechanism
CoM
geom.
center
dCoM = 25 [mm]
contact
load returns through shell → contact → table
MODEL INPUTS / REPOSITORY
mass m = 500 [g] = 0.500 [kg]
semi-axes ≈ 35 × 35 × 40 [mm]
CoM = (0, 0, −25) [mm] from geometric center
contact radius = 35 [mm] · roughness = 0.1 [mm]
shell thickness = 2 [mm]
TORQUE CALCULATION
τg = −m g ℓCoM sin(θ)
θrad = θdeg × π / 180
kg ≈ m g ℓCoM [N·m/rad]
Proxy: m g dCoM = 0.123 [N·m/rad].
Use dCoM for the model; ℓCoM is contact-to-CoM. Measure contact geometry before treating the proxy as physical torque.
BEARING / LOAD CHECK NEXT: load [N] · support spacing [mm] · backlash [deg] · drag [N·m]

## Slide 6
06
Why the egg self-rights
Gravity creates a restoring torque when the center of mass is offset
τg = −m g ℓCoM sin(θ)
τg [N·m]
• m [kg] is total body mass
• g = 9.81 [m/s²] is gravitational acceleration
• ℓCoM [m] is the contact-to-CoM lever arm used in the torque equation
• dCoM [m] is the modeled offset below geometric center; contact geometry remains to be measured
• θ [rad] is tilt from upright; θrad = θdeg × π/180 converts IMU output
Near upright: sin(θ) ≈ θ, so k_g = m g ℓCoM [N·m/rad].
CoM
contact
gravity
F = m g [N]
θ [deg]
measured by IMU
Model example: m = 0.500 [kg], dCoM = 0.025 [m].

## Slide 7
07
The rotational physics
Torque, angular speed, work, and power describe the actuator side
TORQUE AND WORK
τ = r × F
τ [N·m] r [m] F [N]
W = ∫ τ dθ
W [J] θ [rad]
A longer lever arm gives more rotational push for the same force.
SPEED, POWER, AND GEARS
ω = 2π · RPM / 60
ω [rad/s] RPM [rev/min]
Pmech = τ ω
Pmech [W]
Ideal reduction N [-]: ωout = ωmotor / N
τout ≈ ηg N τmotor [N·m]
Gears trade speed for torque; ηg [-] captures loss.
Causal flow: F [N] → τ [N·m] → W [J] → ω [rad/s] → P [W] → geared output [N·m]

## Slide 8
08
Where the energy goes
A command changes electrical energy into motion, storage, and dissipation
Energy transitions make the technical story testable: each arrow names a quantity we can measure or estimate.
ELECTRICAL INPUT
Eelec = ∫ V I dt
V [V], I [A], t [s] → E [J]
MECHANICAL OUTPUT
Pmech = τω
τ [N·m], ω [rad/s] → P [W]
MECHANICAL STATE
K = ½ Jω² [J]
ΔU = m g d(1 − cos θ) [J]
J [kg·m²], d [m], θ [rad]
DISSIPATION
friction + damping
coil heat + sound [J]
EFFICIENCY QUESTION
ηsystem [-] = Pmech [W] / Pelec [W]
Electrical power, output torque, and loaded energy efficiency are not yet measured.
The next experiment instruments Vsupply [V], Isupply [A], torque [N·m], and body response θ [deg].

## Slide 9
09
Individual board communication
First establish one complete board contract; then relay a motion intent to its peer
INDIVIDUAL BOARD CONTRACT
BNO055
I²C SDA 21 / SCL 22
100 [kHz]
ESP32
parses commands
reads sensor
TMC2209
STEP 25 / DIR 26 / ENN 27
VMOT 12 [V]
STEPPER
phase current 0.7 [A]
shaft output
BOARD-TO-BOARD INTENT PATH
EGG A
telemetry
features [deg/s, m/s²]
LAPTOP
filter + sequence
JSON packet
DELAY
250 [ms]
scale 0.50 [-]
EGG B
rock intent
rpm [rev/min]
STATUS: USB peer path is laptop-mediated; direct board-to-board Wi-Fi is next.

## Slide 10
10
Peer coordination
A filtered, delayed, scaled motion intent travels between the two boards
IMU SAMPLE
gyro [deg/s]
accel [m/s²]
FEATURES
‖gyro‖ [deg/s]
adyn [m/s²]
SCORE
0.70 gyro +
0.30 accel [-]
FILTER
EMA τ = 0.18 [s]
hysteresis [-]
FOLLOWER
250 [ms] delay
0.50 scale [-]
gyro_score = clamp(|gyro| / 90 [deg/s], 0, 1)
accel_score = clamp(adyn / 2.5 [m/s²], 0, 1)
I_source = 0.70 × gyro_score + 0.30 × accel_score [-]
I_eff = clamp(3.0 × I_source, 0, 1) × target_fraction [-]
rpm = 60 × I_eff [rev/min]
amplitude = 0.25 × I_eff [shaft rev]
accel = min(30, 30 × I_eff) [rev/min/s]
SAFETY GATES
start ≥ 0.18 [-] stop ≤ 0.10 [-]
stale timeout = 800 [ms]
Peer stale/stop detection exists; motor stop delivery is not yet validated.
Output: I_eff [-] maps to rock command with rpm [rev/min], amplitude [shaft rev], accel [rev/min/s], cycles [-].

## Slide 11
11
Codespace setup and rationale
Parallel layers are joined by explicit interfaces, not a serial software pipeline
SHARED CONTRACT: newline-delimited JSON commands and telemetry
simulator/src/
physics model
metrics
simulator/firmware/
IMU + PWM
state machine
simulator/dashboard/
USB bridge
plots + controls
simulator/dual_board/
filter + delay
peer intent
WHY THIS SPLIT
Test physics without hardware.
Isolate transport from motion.
Trace each run to one command and one log.
Interfaces: physics ↔ experiments; firmware ↔ dashboard; dashboard → peer filter; tests → evidence.

## Slide 12
12
Runtime architecture
Two independent USB channels share the same control contract
WORKING PATH
• Laptop dashboard routes commands by board ID
• Each board emits telemetry at about 30 [samples/s]
• Serial link: 115200 [bit/s] JSON
• USB is the deterministic commissioning transport
OPTIONAL PEER PATH
Laptop-mediated: features → filter → 250 [ms] delay → rock intent.
Both eggs remain independently addressable.
Board commands remain independently addressable.

## Slide 13
13
Wireless next steps
USB works today; Wi-Fi is an experimental HTTP API with unfinished command parity and heartbeat servicing
CURRENT SETUP
USB SERIAL
laptop ↔ ESP32
115200 [bit/s]
JSON
commands + telemetry
newline delimited
DASHBOARD
controls + plots
about 30 [samples/s]
WIRELESS PATH
ACCESS POINT
2.4 [GHz] Wi-Fi
ESP32 HTTP
GET /api/state
POST /api/command
HEARTBEAT
750 [ms] watchdog
PEER RELAY
motion packet
250 [ms] delay
STATUS: USB working · Wi-Fi experimental · command parity + heartbeat pending

## Slide 14
14
Command surface
Every numeric input maps to a physical or timing quantity
INPUT | UNIT | EFFECT
mode | enum | run, smooth run, rock, smooth rock, stable rock (tilt limit)
distance_rev | shaft rev | one-way travel target
amplitude_rev | shaft rev | one-way rock amplitude
rpm | rev/min | peak shaft speed
accel | rev/min/s | speed ramp slope
direction | sign [-] | +1 clockwise, −1 counter-clockwise
cycles | cycles [-] | rock repetitions; 0 means continuous
max_tilt_deg | deg | stable-rock tilt ceiling
intensity | fraction [-] | rock command scale from 0 to 1
target_fraction | fraction [-] | peer follower scale; default 0.50
Actions without numeric inputs: tare IMU, stop, stop immediately, record origin, return to origin.

## Slide 15
15
Dashboard measurements
The UI exposes orientation, inertial, thermal, and motor state
IMU MEASUREMENTS
heading / yaw
orientation about vertical
[deg]
roll, pitch
body orientation relative to tare
[deg]
accel x / y / z
specific force, includes gravity
[m/s²]
gyro x / y / z
angular velocity
[deg/s]
temperature
sensor / board thermal reading
[°C]
calibration
BNO055 status per subsystem
[0–3]
MOTOR AND TIMING STATE
rpm / target_rpm
shaft speed / target
[rev/min]
accel_rpm_s
speed ramp
[rev/min/s]
position_steps
commanded position
[steps]
distance_rev
commanded travel
[shaft rev]
target_steps
finite travel target
[steps]
step_rate_hz
STEP pulse rate
[steps/s]
t_ms
sample timestamp
[ms]
telemetry_hz
stream rate
[samples/s]
Position is generated-step state; IMU angles are body orientation.

## Slide 16
16
Physics vocabulary in the dashboard
Raw sensor fields become interpretable motion features
GYROSCOPE
ω [deg/s]
Angular velocity.
Large magnitude means rapid rotation.
ACCELEROMETER
a [m/s²]
Specific force.
A still sensor is near g = 9.81 [m/s²].
DYNAMIC ACCEL
adyn [m/s²]
Motion beyond gravity.
adyn = |‖a‖ − g|.
EULER ANGLES
yaw / roll / pitch [deg]
Orientation coordinates.
Tare makes them relative to a pose.
Peer detection uses gyro magnitude first, then dynamic acceleration to reject a stationary tilt.

## Slide 17
17
Motion primitives and conversion
The firmware commands shaft travel; the mechanism determines the resulting tilt
RUN
one-way travel
to distance_rev
SMOOTH RUN
one-way travel
with braking
ROCK
alternate direction
for cycles
TILT-LIMITED ROCK
continuous motion
with over-tilt safety
200 [full steps/rev] × 16 [microsteps/full step] = 3200 [commanded steps/rev]
step_rate = RPM × 3200 / 60
step_rate [steps/s] RPM [rev/min]
DISTANCE (SHAFT)
0.05
rev
COMMANDED TRAVEL
160
steps
COMMANDED SHAFT ANGLE
18
deg

## Slide 18
18
Smooth distance control
Braking begins before the endpoint so the command does not cut off at cruise speed
REMAINING STEPS [steps] ↓
braking_rpm = sqrt(
remaining_steps × 120 × accel / steps_per_rev)
target_rpm = min(cruise_rpm, braking_rpm)
step_rate [steps/s] =
target_rpm × steps_per_rev / 60
CONTROL LAW
120 = 2 × 60 [s/min] remaining_steps [steps] accel [rev/min/s] steps_per_rev [steps/rev]
NORMAL RUN
RAMP
CRUISE
CUT
SMOOTH RUN
RAMP
CRUISE
BRAKE
SETTLE
The input is a speed ramp; the output is lower endpoint impulse.

## Slide 19
19
Firmware realization
A small state machine turns JSON fields into bounded pulse timing
JSON PARSER
command + numeric fields [units]
STEPPER STATE
mode + position [steps]
PWM OUTPUT
STEP [steps/s] + DIR + ENN
TELEMETRY
IMU + motor state / 33 [ms]
if mode == "smooth_run":
remaining = target_steps - abs(position_steps)
target_rpm = min(cruise_rpm, braking_rpm(remaining))
step_pwm.freq(round(target_rpm * 3200 / 60))
Configured ceilings
1–240 [rev/min] 1–120 [rev/min/s] 15,000 [steps/s]

## Slide 20
20
Measured command-path evidence
Physical log from unloaded-board USB commissioning
GENERATED TARGET
160
steps
USB CMD→IDLE
110–113
ms
GENERATED CIRCLE
±3200
steps
SENSOR TEMP
31–32
°C
KEY READOUT
4 [rev/min] · 0.05 [shaft rev] → software auto-stop at 160 [steps] → pitch peak 3.06 [deg] · gyro peak 13.73 [deg/s]
Command path observed: parse → auto-stop → reversal → telemetry → 0.110 [s] stop response.

## Slide 21
21
What the current evidence measures
Separate generated motion, sensed body motion, and physical load
OBSERVED NOW
• Generated position [steps] and travel [shaft rev]
• BNO055 orientation [deg], gyro [deg/s], accel [m/s²]
• USB stop response [ms]
• Unloaded-board temperature [°C]
INSTRUMENT NEXT
• Physical shaft angle [deg] with marker or encoder
• Motor phase current [A] and VMOT [V]
• Loaded tilt amplitude [deg] and natural frequency [Hz]
• Repeatability [%] and missed-step count [steps]
PRODUCT QUESTION
• Can the body hold a target tilt [deg]?
• What load [g] and torque [N·m] remain stable?
• What temperature rise [°C] occurs over duty time [s]?
• Does peer delay [ms] feel intentional?
Key gap: commanded shaft motion [steps] versus verified physical shaft motion [deg].
Validated: unloaded USB command path. Not yet validated: loaded tilt, physical shaft angle, torque, power, final gear ratio, or wireless reliability.

## Slide 22
22
Next experiment
Close the command-to-motion gap with an instrumented loaded run
01
POWER
VMOT [V]
logic [V]
02
SHAFT
marker / encoder
angle [deg]
03
LOAD
mass [g]
CoM offset [mm]
04
CORRELATE
tilt [deg]
current [A]
temperature [°C]
Acceptance output
commanded steps [steps] ↔ measured shaft angle [deg] ↔ body response [deg/s, m/s²]
• Repeat at conservative speed: 3–10 [rev/min]
• Sweep acceleration: 5–30 [rev/min/s]
• Record current [A], temperature [°C], tilt [deg], missed steps [steps] over time [s]

## Slide 23
23
Making the wobble feel cute
Precise control turns mechanical parameters into a motion language
CUTE IS A CONTROLLED GESTURE
parameter → command → measured response → perceived quality
amplitude
size [shaft rev]
small = contained
rpm
tempo [rev/min]
low = gentle
accel
softness [rev/min/s]
slow ramp = soft
cycles
persistence [count]
brief = expressive
delay
social timing [ms]
late reply = character
intensity
command scale [-]
reduced = tender
θbody(t) = A · E(t) · sin(2π fw t + φ)
A [deg] fw [Hz] E [-] t [s] φ [rad]
rpm [rev/min] sets motor tempo; fw [Hz] is measured body response.
AUTHORING FLOW
ANTICIPATE
low speed
small ramp
WOBBLE
bounded tilt
measured [deg]
SETTLE
smooth brake
short dwell [s]
ART / USER EXPERIENCE
The dashboard authors the gesture.
The egg is the visible character.
A second egg makes it social.
Hypothesis until measured.
Design direction: use variation and delay to make control feel alive.

## Slide 24
24
What I learned
A first serious hardware build grew out of a software and installation practice
STARTING POINT
Most of my background is in software, digital and user-experience design, and art installations.
This project moved that practice into sensing, wiring, motion, and physical feedback.
THE HARDWARE LESSON
This was the first time I soldered since my first year of college.
I found the work incredibly rewarding and meditative, and I feel very blessed to have had the best mentors.
Thank you to the lab for providing tools so generously. I definitely consumed a lot of 3D-printing resources.
The technical result is a working prototype. The personal result is a wider practice.

## Slide 25
25
Photos and meals
Space for process documentation and the shared studio life around the build
FIRST SOLDERING / PROCESS
WIRING + DEBUGGING
3D PRINT ITERATIONS / RESOURCES
MEALS / MENTORSHIP

## Slide 26
26
Reproducibility
Source map for the deck, video, and prototype
BUILD
python3 simulator/docs/build_google_slides_deck.py
# output: simulator/docs/WOBBLE_MECHANISMS_TECHNICAL_DECK_post_critique.pptx
PRIMARY REFERENCES
simulator/docs/TECHNICAL_PRESENTATION.md
simulator/docs/PHYSICS_TALKING_OUTLINE.md
simulator/docs/CAD_IMPORT_GUIDE.md
simulator/src/egg_model.py
simulator/wired_tests/physical_test_log.md
simulator/firmware/main.py
simulator/dashboard/index.html
simulator/dual_board/ripple_logic.py
RASTER ASSETS
simulator/docs/assets/png/
system-architecture.png
physical-validation.png
egg-unit-sheet1-schematic-focus.png
COMPANION VIDEO
simulator/ripple_3d/output/
ripple_4x4.mp4
Explanatory only: not calibrated rigid-body dynamics.
Technical flow: model → command → pulse → motion → measurement.